## Slide 1: Accelerate Convolutional Neural Network
Ezekiel Tay z5378748
Kenneth Law z5363506
Sicheng Jin z5317861

## Slide 2: Project Overview
Objective: Investigate the performance gains of accelerating convolution layers in CNN inference using FPGA.
Context: CNN convolution layers are compute-intensive to deploy on low-energy/cost embedded systems. Often taking over 90% of runtime on deeper models.
Project Scope: Implement a CNN ("ToyCNN") on the Kria KV260 board, leveraging both CPU (PS) and FPGA (PL) to classify handwritten digits of the MNIST dataset
Result: Achieved a ~82% inference speedup, with the convolution layer accelerated by a factor of ~140x.

## Slide 3: Quick Recap on CNNs
A Convolutional Neural Network is a class of neural networks that specializes in processing data containing spatial features, such as an image.

## Slide 4: ToyCNN
Convolution layer -> (main target of speed ups)
Activation layer (Relu)
Flattening
Fully connected layer

## Slide 5: Aims and Goals
Develop a lightweight CNN inference pipeline for handwritten digit classification (Data from the MNIST dataset)
Examine the baseline SW implementation performance
Leverage the strengths of both Processing System (PS) and Programming logic (PL) to minimise latency via hardware/software co-design
  Eg. Offload the expensive convolution operations to FPGA logic
Compare performances on the KV260 board

## Slide 6: Results
An accelerated design was achieved!
Baseline (SW-only):
  ~43.1s to classify 10,000 images
  Averaging 4.31ms per image
HW+SW version:
  ~23.6s to classify 10,000 images
  Averaging 2.36ms per image
140× convolution layer speed-up, ~82% total runtime reduction.

## Slide 7: AI Usage
Assist in developing the python code for the training process to obtain the weights and biases.
Generating C++ code for the 3-line buffer (Sliding image across kernels instead of kernels across image)
Debugging why unrolling the dot product loop didn’t synthesise an adder tree
  Floating-point addition is non-associative due to rounding
  HLS does not create adder tree by default
  Introduced manually

## Slide 8: Design
Solution approach
Model
  A custom small CNN trained on MNIST
  Layers:
    Conv: 8 3x3 kernels
    ReLU
    Flatten
    FC: 10 nodes, 5,408 connections each
  PyTorch was used for training
    99.88% train accuracy
    97.82% test accuracy
    Trained weights were exported to C++ headers for inference code.

## Slide 9: Baseline Design
Baseline Design
SW-only side
  ALL operations are done on the CPU

## Slide 10: Accelerated Design
Solution approach
SW (CPU) side
  Handle the image preprocessing and data movement via memcpy
  Pilots the FPGA
  Leverage the CPU’s fast sequential processing power to compute the FC layer

## Slide 11: Accelerated Design
Solution approach
HW (FPGA) side
  Leverage the FPGA’s parallel processing power to perform convolution
  Key components are:
    Convolution Multiply Accumulate (CMAC)
    3-line image buffer
    Parallel data writers to the output feature map

## Slide 12: Accelerated Design
Solution approach
HW (FPGA) side
  Used the AXI-Lite interface to transfer data to and from the PS and PL sides with a shared memory space (35.6KB shared data)

## Slide 13: Accelerated Design
HW Resource utilization
1586 cycle latency (est. 15.86us)
Nearly a third of the DSPs, FFs and LUTS and only 11% of the BRAM

## Slide 14: Accelerated Design
Block Design
  Used the AXI-Lite interface to transfer data to and from the PS and PL sides with a shared memory space

## Slide 15: Results
Performance Evaluation
82% overall gains
Convolution layer accelerated by 140x
HW+SW solution closely matched synthesis estimates (15.86us)

## Slide 16: Discussion
Speedup:
Significant performance gains to the convolution layer of over 140x
Demonstrating effective usage of FPGA parallel processing power
Limitations:
Amdahl’s law: Convolution is no longer the bottleneck
Data movement and remaining layers, especially FC dominate runtime
Scalability:
Greater benefits expected for deeper CNN architectures

## Slide 17: Conclusion - What worked?
Efficient Hardware Acceleration:
  CMAC
    8 fully pipelined CMAC units with II=1 working in parallel provided high throughput and fast convolution operations
  3-Line Image Buffer
    3-line image buffer eliminated the need to slide the kernels in each CMAC, instead sliding the image under the kernels
    Reduced redundant duplicate computations and allowed CMAC units to remain simple and efficient
  Parallel Output Writers
    Each feature map for each kernel was written in parallel by 8 output writer modules
    Avoiding bottlenecks in writing large amounts of data back to memory.
  Shared Memory Optimisation via AXI-Lite
    Although basic, throughput was maximized by
      Partitioning arrays for full parallel access
      Aligning memory into 128B and 4KB blocks for efficient memcpy’s for PS and PL data transfer
  Inference accuracy preserved
    Used float operations to maintain model accuracy.

## Slide 18: Conclusion - What didn’t work?
  AXI-Stream
  Originally planned, but technical difficulties arose… Meaning we abandoned the ping pong buffer
  Flatten & FC Layer in SW
  Since the conv layer freed up CPU time, the flatten and FC layers filled in, taking up 25.82% and 64.21%, respectively.
  This is NOT due to FPGA data writing overhead, but memory intensive operations

## Slide 19: Conclusion - What didn’t work?
  Fixed-Point Arithmetic
  Although changing from floating point to fixed point could further reduce FPGA resources and latency, decided to skip this endeavour
  Early results indicated bottlenecks were elsewhere
    Even if we pursued this, Amdahl’s law would make the overall gains negligible (FPGA already only takes up 0.72% of runtime)
    Not worth negligible gains at the cost of accuracy loss
  FFT-based Convolution
  Only feasible for large networks
  Software & Toolchain Difficulties
  Significant pain and suffering using the Xilinx tools (especially Vivado HLS 2020.1), particularly due to version mismatches.
  Lots of time wasted, slowing development
  Our solution: Use Vitis HLS 2021.2!
  XSCT only worked on Stefan’s computer for some reason

## Slide 20: Conclusion – If given more time
Model quantisation during training
  Fixed point weights generated during TRAINING
Runtime reconfigurability
  Opens ability to run models with multiple convolutional layers
AXI stream implementation
  Dataflow design with ping pong buffers
  Potentially decreasing the flatten layer runtime as the output gets streamed into it

## Slide 21: Conclusion – If given more time
Software Algorithms
  Winograd
    Divide the whole input image into 4*4 chunks
    Pre-calculate and store the optimal matrices for 4*4 input
    Saves 50% of calculations
  Wallace Tree
    Concept discovered during our preparation for the seminar
    Speed up the multiplication of binary numbers by efficiently summing partial products.
    Reduce the carry propagate delay
    Reduce the number of adders
    Potentially decrease the LUT usage as seen in research papers

## Slide 22: Thank You